## Slide 1
PROGRESS REPORT · AUGUST 2026
IO-Aware Top-Level Placement
GPU global placement for 10M–30M-cell designs that minimizes cross-region IO and pure feed-throughs
DREAMPlace-based · dev on NVIDIA L4, target H100 · Phase 1: fixed regions, count-based objectives
Notes: 開場：題目是 10M–30M cell 的 top-level placement，region 幾何由設計者給定，目標是最小化跨 region 的 IO 穿越數與 pure feed-through 數（都是「計數」而非線長），在 DREAMPlace 上用 GPU 完成。

## Slide 2
AGENDA
Outline
1
Previous Works
7 papers · feed-through-aware planning line + GPU analytical placement line, one slide each
2
Benchmark
the 1M / 5M / 10M / 30M ladder, region overlay, and realism gates
3
Algorithm Flow
Phase-1 pipeline + what M0/M1 already built and taught us
4
Experiments
two comparison tracks: per-region commercial P&R, and flat DREAMPlace
Notes: 今天四個部分：先盤點七篇相關工作（含老師指定的 GrandPlan 與 ASP-DAC'24 那篇），再講 benchmark 階梯、演算法流程與 M0/M1 現況，最後是兩個實驗設計。

## Slide 3
PROBLEM
Problem Formulation (Phase 1)
Given
Flat netlist at 10M–30M standard cells (macros fixed in Phase 1)
K = 4–32 exactly-abutted partition regions — geometry is a fixed input (channelless style)
Optimize placement to minimize
IO count — crossings of region boundaries by each net's routing tree (MST / RSMT proxy)
Pure feed-throughs — tree passes a region where the net has no pin
… while preserving wirelength (HPWL) and legality
Output
Placement + induced block→region membership + per-net IO / FT report
Counts, not wirelength
Regions fixed, membership free
GPU end-to-end
R1
R2
R3
R4
pure feed-through: net has no pin in R4
● boundary crossing (IO)
Notes: 用右邊的圖解釋兩個指標：橙點是 tree edge 穿越 region 邊界（IO）；紅色 net 從 R3 繞到 R2，途中穿過沒有 pin 的 R4，那一段就是 pure feed-through。強調：我們優化的是離散計數，region 幾何不動，動的是每顆 cell（亦即 block 歸屬）。

## Slide 4
PREVIOUS WORKS
Two Research Lines — and the Gap We Target
Line A · Feed-through-aware top-level planning (module granularity, ~10² blocks)
GrandPlan · ISPD'26
FTAFP · ASP-DAC'25
Flora · arXiv'25
FT insertion · ISQED'25
HiDaP · TCAD'21
Decide region geometry / module shapes; minimize cross-partition wirelength or module-level FT
Line B · GPU analytical placement engines (cell granularity, 10⁶–10⁷ cells)
DREAMPlace · DAC'19/TCAD'21
3.0 fence regions · ICCAD'20
4.0 net weighting · TCAD'23
RTO placement · ASP-DAC'24
Place cells at scale on GPU; objectives are wirelength / density / timing — no cross-region IO or FT notion
This work — the intersection neither line covers
Cell-granularity GPU placement with count-based objectives (boundary-crossing IO #, pure-FT #) under fixed region geometry at 10M–30M. Our survey found no prior differentiable pure-FT model and no per-net tree-crossing evaluator at this scale.
Notes: 定位：兩條線——模組粒度的 FT-aware 規劃（決定幾何）與 cell 粒度的 GPU 引擎（不懂 IO/FT）。我們做的是交集：幾何固定、優化離散計數、cell 粒度、3000萬規模。兩個 novelty claim：可微分 pure-FT 模型與 MST tree-crossing evaluator。

## Slide 5
PREVIOUS WORKS · 1 / 7
GrandPlan — Differentiable Top-Level Floorplanning + Partition-Level Placement
ISPD 2026
NVIDIA Research + UT Austin
closest work
Key idea
GPU-accelerated, differentiable, end-to-end co-optimization of top-level floorplan and partition-level cell placement (custom CUDA kernels)
Produces clean rectilinear, exactly-abutted partition boundaries while concurrently placing macros + standard cells
Method — 3 coupled stages
Flat IP-core placement with differentiable grouping objectives
Partition-boundary refinement via simulated annealing under area / routability constraints
Routability-aware fence-region placement
Results
8 industrial IP-cores up to 25M cells: total WL up to −14%, cross-partition (feed-through) WL −27% avg vs expert manual floorplans; ≈1.2 h runtime
vs. Ours
Region geometry is their output — in our setting it is a fixed designer input
They minimize cross-partition wirelength; we minimize discrete counts (IO crossings, pure FT) with an exact per-net tree evaluator
No public code → conceptual reference, not a runnable baseline
Z. Xiong, Y.-C. Lu, D. Z. Pan, H. Ren, “GrandPlan: Differentiable, Simultaneous Top-Level Floorplanning and Partition-Level Cell Placement for Large-Scale IP-Cores,” ISPD 2026, pp. 64–72.
Notes: 最接近的對手（NVIDIA）。差異要講清楚：他們連 region 幾何一起優化、目標是跨區線長；我們 region 固定、目標是計數（IO/FT）。風險：題目碰撞 → 盡快把 M1/M2 證據發表出去。

## Slide 6
PREVIOUS WORKS · 2 / 7
Analytical Placement with Routing-Topology Optimization
ASP-DAC 2024
Fuzhou University
ext. Integration (VLSI J.) 2025
Key idea
HPWL-driven placers ignore each net's internal routing topology → gap between estimate and routed wirelength
Build a differentiable wirelength model on the ideal RSMT topology inside global placement; segment screening / tracing yields meaningful gradients for interior points
Method
RSMT-based differentiable WL in GP, then post-GP cell refinement with swift density control
Results
ICCAD-2015 suite: routed WL −3%, HPWL −0.8%, TNS −23.8% vs a state-of-the-art analytical placer
vs. Ours
Same recipe shape as ours: a tree-topology term inside analytical GP, periodically re-anchored by an exact evaluator
But the objective is routed wirelength — region-oblivious, no IO / FT notion
Validates that per-net tree objectives can drive GP gradients at scale
M. Wei, X. Tong, Z. Cai, P. Zou, Z. Lin, J. Chen, “An Analytical Placement Algorithm with Routing Topology Optimization,” ASP-DAC 2024, pp. 294–299 (extended: Integration, vol. 100, 2025).
Notes: 老師指定的第二篇。它證明「在 GP 裡放 tree-topology 目標」可行，和我們的 MST-crossing 回饋同一個精神；但它優化的是 routed WL，沒有 region 概念。可順帶提 2025 年的 looking-ahead 期刊擴充版。

## Slide 7
PREVIOUS WORKS · 3 / 7
FTAFP — Feedthrough-Aware Floorplanner for Large-Scale SoCs
ASP-DAC 2025
BUPT + Huawei + CUHK
Key idea
In hierarchical SoC reuse, a feed-through is a through-module connection that adds buffers + ports inside the reused module → congestion and timing damage
Few prior works model FT at all — FTAFP optimizes it explicitly at the floorplan stage
Method
Feed-through-aware floorplanning for hierarchical large-scale SoCs: module shapes / positions co-optimized with an explicit FT cost (module granularity)
Why it matters to us
Confirms FT as a first-class objective in 2025 academic work, at the granularity directly above ours
vs. Ours
Optimizes ~10² module shapes and positions; we place 10⁷ cells with region geometry fixed
FT counted between modules; ours is per-net tree-based, plus boundary-pin (IO) demand
Z. Li, K. Tian, J. Zhai, Z. Li, S. Kai, S. Xu, B. Yu, K. Zhao, “FTAFP: A Feedthrough-Aware Floorplanner for Hierarchical Design of Large-Scale SoCs,” ASP-DAC 2025, pp. 886–892.
Notes: 重點：FT 的定義——穿過模組的連線要在模組內部加 buffer 和 port，傷 routability 與 timing。這是我們 pure-FT 指標的工業動機。層級在我們上方（floorplan），互補不衝突。

## Slide 8
PREVIOUS WORKS · 4 / 7
Flora — “One Step Beyond”: Feedthrough & Placement-Aware Rectilinear Floorplanning
arXiv 2025 (2507.14914)
USTC + Huawei Noah's Ark
Key idea
Floorplanning decided in isolation from later placement → suboptimal placement and excessive feed-through; Flora couples the two
Method — 3 stages
Wiremask + position-mask co-optimization of HPWL and FT
Fixed-outline, zero-whitespace module resizing that refines FT and placement
Tree-search component positioning inside modules, then boundary adjustment
Results
HPWL −6%, FT-pin −5.2%, FT-module −29.2%, component placement +14% vs SOTA
vs. Ours
Still module-level rectilinear floorplanning (learning / search based)
Shows FT + placement coupling is an active 2025 topic — but no GPU-scale cell placement, no count-exact evaluator
Z. Xu, J. Wang, S. Xu, Z. Geng, M. Yuan, F. Wu, “One Step Beyond: Feedthrough & Placement-Aware Rectilinear Floorplanner,” arXiv:2507.14914, 2025.
Notes: 第三篇 FT 系譜：Flora 把 floorplan 與 placement 耦合，前瞻性和 GrandPlan 同方向；但仍是模組粒度。FTpin/FTmod 的指標切法可以引用來對照我們的 per-net 計數。

## Slide 9
PREVIOUS WORKS · 5 / 7
Feedthrough Insertion Methodology for Hierarchical SoCs
ISQED 2025
industry methodology
Key idea
In channel-based hierarchical SoCs, top-channel congestion sets die area; feed-through insertion at the floorplan stage decongests top channels → die-area savings
Manual / flattened FT insertion breaks down at scale: huge top-level connection counts, RTL coupling, sub-chip port porting, logical-equivalence checkout
Method
An automated feed-through insertion methodology integrated into the hierarchical implementation flow
Relation to our setting
Channel-based and channelless are the two hierarchical integration styles — our Phase-1 cost model is channelless (fully-abutted regions), with a channel-style cost switch planned for Phase 2
Every feed-through our placement avoids is one this methodology never has to insert
vs. Ours
Downstream remedy — inserts the FTs a design already needs
We act upstream: placement chooses membership so fewer FTs exist at all
Industrial evidence that FT count is a first-order cost (die area, TAT)
R. Sakariya, S. Aich, V. Joshi, R. Griesmer, “Die Area Reduction by Decongesting Top Channels Using Novel Feedthrough Insertion Methodology in Hierarchical SoC Designs,” ISQED 2025.
Notes: 這篇是產業證詞：FT 直接影響 die area 與 turnaround。定位：他們在下游插 FT，我們在上游減少 FT 的需求。也呼應我們 channelless 設定以外的 channel-based 變體（Phase 2 的 cost-model switch）。

## Slide 10
PREVIOUS WORKS · 6 / 7
HiDaP — Multilevel Dataflow-Driven Macro Placement from RTL Structure
IEEE TCAD 2021
UPC Barcelona + eSilicon
Key idea
RTL hierarchy + dataflow affinity (register latency, flow width) encode designer intent that flat synthesis discards — use them to drive multilevel macro placement
Method
Hierarchy tree → blocks of macros + std cells; top-down slicing-structure layout; adaptive multi-objective cost (WL, timing, overlap, preferred locations) with spectral / force-directed hints
Results
Large industrial designs: beats commercial + academic macro placers and expert handcrafted floorplans on WL & timing; near closure post-route
vs. Ours
Top-level planning at macro / block granularity, no explicit IO or FT count objective
Supports our benchmark premise: RTL hierarchy ≈ natural physical regions (our region ground truth on real designs)
A. Vidal-Obiols, J. Cortadella, J. Petit, M. Galceran-Oms, F. Martorell, “Multilevel Dataflow-Driven Macro Placement Guided by RTL Structure and Analytical Methods,” IEEE TCAD 40(12), 2021.
Notes: 這篇支持我們的 benchmark 前提：RTL 階層就是天然的 region 邊界（tile/group/cluster）。它自己是 macro 粒度、沒有 IO/FT 計數目標。

## Slide 11
PREVIOUS WORKS · 7 / 7
DREAMPlace Lineage — the Engine We Build On
1
DREAMPlace
DAC 2019 / TCAD 2021
Casts ePlace/RePlAce electrostatic GP as “training a neural net” on CUDA tensors — 30×+ GP speedup, 10M-cell global placement in minutes. Lin, Jiang, Gu, Li, Dhar, Ren, Khailany, Pan.
2
DREAMPlace 3.0
ICCAD 2020
Multi-electrostatics fence-region placement (region constraints) — the machinery behind our two-stage baseline. Gu, Jiang, Lin, Pan.
3
DREAMPlace 4.0
DATE 2022 / TCAD 2023
Timing-driven, momentum-based net weighting — the net-weight mechanism our M1 IO-reweighting repurposes. Liao, Guo, Guo, Liu, Lin, Yu.
vs. Ours — engine, not competitor
None of the lineage sees cross-region IO / FT. Our integration: a 5-line iteration callback + region / evaluator stack on top — the fork is otherwise untouched.
Y. Lin et al., TCAD 40(5) 2021 · J. Gu et al., ICCAD 2020 · P. Liao et al., TCAD 42(10) 2023.
Notes: DREAMPlace 家族是引擎：1.0 給 GPU 規模，3.0 給 fence-region 機制（two-stage baseline 用），4.0 給 net-weighting 機制（M1 reweighting 借用）。我們對 fork 只加了 5 行 iteration callback 與 shapely 相容兩個 patch。

## Slide 12
BENCHMARK
The 1M → 30M Benchmark Ladder
Tier | Design / source | Scale | Status
1M-class | ISPD'05/06 bigblue4 · newblue7; ISPD'15 superblue12 (LEF/DEF, real fences) | 2.18M / 2.51M / 1.29M cells | In use — M0/M1 numbers on adaptec1 (0.21M) + bigblue4
5M | MemPool half-cluster ≈ 2 × mempool_group (NanGate45, OpenROAD flow) | ≈5.7M (group ≈ 3.1M) | To assemble — lowest priority of the four
10M | ISPD 2025 mempool_cluster — full LEF/DEF/LIB/SDC + placed DEF | 11.31M cells / 12.71M nets | On disk (46 GB suite) — golden workhorse
30M | TeraPool reduced (open RTL; ISPD'24 simplified format reaches ≈50M) | ~30M target | To build — moderate effort
Region overlay: grid {2×2 … 8×4} + seeded random slicing, snapped to a 512² lattice (exact counting), K ∈ {8, 16, 32}; real designs later use DEF REGION/GROUP with RTL-hierarchy ground truth (tile / group / cluster)
Realism gate: naive replication forbidden (cut collapses to 0, Rent p → 0) — every augmented case checked with RentCon, target p ≈ 0.6–0.75; fallbacks: Rent-gap glue nets, ArtNet synthesis
Experiment matrix: scale × K × region-type; ≥3 seeds at 1M; report IO, pure-FT, HPWL / tree-WL, GP runtime, peak GPU memory
Notes: 誠實說明：目前實際跑過的只有 adaptec1 與 bigblue4；10M 的 mempool_cluster 已下載在手（46GB），30M 要自己組。重點在 realism gate：不能盲目複製，要過 Rent exponent 檢查，否則 IO 會假性歸零。

## Slide 13
ALGORITHM FLOW
Phase-1 Pipeline
0 · Inputs & preprocess
Netlist + K partition regions (fixed geometry) → 512² region-id grid + boundary table; Mt-KaHyPar warm start
1 · GPU global placement
DREAMPlace 4.x fork: min WA-WL + λ_D·density + λ_IO·L_IO + λ_FT·L_FT + λ_pin·L_pincap
2 · Decode
Soft membership → hard assignment (conditional expectation)
3 · Refine
Boundary-local trial moves / bin-FM
4 · Output
Placement + block→region membership + per-net IO/FT report
Only stage 1 runs inside DREAMPlace (our fork: added objective terms + a 5-line iteration callback); stages 0 / 2 / 3 / 4 are our own code around the engine.
Evaluator loop (inside stage 1) — every N = 50–100 iterations · a feedback signal, not a stopping gate (GP stops on DREAMPlace convergence)
GPU MST per net (degree-bucketed batched Prim)
Boundary crossings via 2-D prefix sums — O(1) per edge
FT via K-bit region masks: popcount(passed & ~pins)
Feed back: report · λ re-normalization · per-net weights
implemented (M0/M1)
partial — differentiable IO/FT = M2/M3
planned
↳ Downstream (Exp. 1): final block→region membership → per-region P&R with Innovus → assembled top-level QoR (routed WL · timing · congestion)
Notes: 歸屬關係要講清楚：五格裡只有 stage 1 在 DREAMPlace（我們的 fork：加目標項 + 5 行 iteration callback）；stage 0/2/3/4 都是我們自己的 code。Evaluator 每 50–100 iteration 介入一次（開銷 <2.5%），是回饋訊號（報表 + λ 正規化 + per-net 權重），不是「IO 達門檻就停」的檢查——停止仍由 DREAMPlace 收斂決定。GP 產出的是 softmax 軟歸屬，所以需要 decode（軟→硬指派）與 refine（邊界模糊 cell 清理），這兩步是 M2 之後的我們的規劃。最後的 per-region Innovus P&R 是下游實作/驗證，即 Exp 1。設計選擇：region 幾何固定 + 位置誘導歸屬 ⇒ 主流程一個 global density field 就夠。

## Slide 14
ALGORITHM FLOW
Status & Evidence — M0 + M1 Complete (13/13 tasks)
Built & verified (33+ unit tests)
Exact GPU evaluator: per-net MST + prefix-sum crossings + bitmask FT — bit-matches the CPU golden on every count
Warm evaluate 0.16 s (adaptec1) / 1.32 s (bigblue4); 174× vs CPU on a 2M synthetic; <2.5% of placement runtime
Baselines: flat DREAMPlace + post-hoc counting; two-stage Mt-KaHyPar → greedy+2-opt region mapping → fence-constrained placement
Net-reweighting closed loop via a 5-line DREAMPlace callback: w = 1 + α·min(crossings, cap)
Evidence → next step
M0: two-stage IO = 1.2–1.8× flat although its min-cut bound is at or below flat → the loss sits in the “hypergraph cut → geometric tree crossings” translation. That gap is the research target.
M1: reweighting cuts pure-FT −10% … −49% at HPWL +≈1%, but IO best −0.06% (run noise ±1%) → WL weights compress paths; they cannot flip region membership
⇒ M2: differentiable soft membership (softmax over region distances, τ annealing) to give the “which region” decision a gradient
174×
evaluator speedup vs CPU (2M case)
−49%
pure-FT on bigblue4, HPWL +1%
±1%
run-to-run IO noise → multi-seed needed
<2.5%
evaluator share of loop runtime
Notes: 這頁是核心：M1 的負面結果要誠實講——reweighting 只壓得了 FT（路徑緊實度），壓不動 IO（離散歸屬），而且單 seed 噪聲 ±1% 比效果大一個量級。這直接導出 M2 要給「哪個 region」一個可微分的梯度。M0 的發現：問題不在 partition 品質，在 cut→幾何 crossing 的轉換損失。

## Slide 15
EXPERIMENTS · 1 / 2
Exp. 1 — Designer Regions + Per-Region Commercial P&R
PROPOSED
Arm A · Baseline — designer flow
Designer floorplan: region geometry + block→region membership
Per-region P&R with Innovus (identical scripts / constraints / effort)
Assemble → top-level metrics
Arm B · Ours — membership re-decided
Same region geometry; our GPU IO-aware placement re-decides block→region membership
Per-region P&R with Innovus (identical scripts / constraints / effort)
Assemble → top-level metrics
Held fixed across arms: region geometry (byte-identical) · tech/LEF/lib/SDC · Innovus version, scripts, effort, seeds · per-region utilization caps · the same IO/FT evaluator for both arms
Compare: routed WL · WNS / TNS · # feed-through nets & ports · top-channel congestion / DRC · per-region utilization · turnaround time
Needs: a testcase with a real designer floorplan + Innovus access. Worth adding a third arm — IO-agnostic assignment (greedy+2-opt) — to isolate “IO-aware” from “any optimization”.
Notes: 實驗一（提案，repo 尚無 Innovus flow）：設計者給定 region 與歸屬當 baseline；我們只重新決定「哪個 block 放哪個 region」，幾何與 P&R 腳本完全不動，再用同一套 Innovus 流程比 QoR。關鍵公平性：per-region utilization 要鎖住，否則贏的可能是容積重分配而非 IO-awareness。需要老師協助：有 designer floorplan 的 testcase 與 Innovus license。

## Slide 16
EXPERIMENTS · 2 / 2
Exp. 2 — vs Region-Oblivious Flat DREAMPlace
Flat DREAMPlace
no region knowledge; post-hoc IO/FT counting
Two-stage
Mt-KaHyPar partition → fence-constrained placement
Ours
IO-aware GP (M1 reweighting → M2 differentiable)
Preliminary (bigblue4, K=16 grid, single seed — M1 reweighting only)
Metric | flat | two-stage | ours (M1) | Δ vs flat
IO count | 100,108 | 178,594 | 100,736 | +0.6% (≈ noise)
Pure feed-throughs | 7,045 | 77,899 | 3,585 | −49.1%
HPWL | 748.5 M | 4,459.8 M | 756.2 M | +1.0%
Runtime (s) | 545 | 3,738 | 535 | −2%
Read with care
single seed; IO noise ≈ ±1%
reweighting only — M2 differentiable membership is the lever for IO
Protocol: scales 1M → 30M × K ∈ {8,16,32} × {grid, rectilinear}; ≥3 seeds at 1M; identical configs & iteration budgets across arms; regions frozen before any run
Fairness: co-report HPWL / runtime / memory (never IO alone); report the full λ-sweep Pareto, not a single tuned point
Notes: 實驗二：跟完全不看 region 的 flat DREAMPlace 比（另加 two-stage 當中間梯）。現有數據誠實呈現：FT 大降 49% 但 IO 持平（單 seed，噪聲 ±1%）；M2 才是要壓 IO 的機制。強調公平性協定：同 config、同 iteration 預算、region 跑前凍結、报 Pareto 而非單點。

## Slide 17
SUMMARY
Where We Are, and What We Need
Related work: feed-through optimization is hot in 2025–26 (GrandPlan, FTAFP, Flora) — but all module-granularity or wirelength-based; the count-based, cell-level, fixed-region formulation is open
Benchmark ladder 1M → 30M defined; 10M ISPD'25 mempool_cluster already on disk; Rent-exponent realism gate for every augmented case
M0 + M1 complete: exact GPU evaluator (174×, <2.5% overhead); negative reweighting result diagnosed → M2 differentiable membership is the next lever
Two experiment tracks specified: designer regions + per-region Innovus P&R (membership swap only), and region-oblivious flat DREAMPlace with a frozen-region, multi-seed, Pareto protocol
Asks
A testcase with a real designer floorplan + Innovus access (Experiment 1)
H100 allocation for the M4 scale-up runs (10M / 30M)
Feedback on the benchmark-credibility plan: region sources, multi-seed budget
Notes: 結尾：三個請求——Innovus testcase、H100 時段、benchmark 公信力計畫的意見。若老師問進度風險：最大風險是與 NVIDIA GrandPlan 的題目碰撞，因此 M1/M2 的證據要盡快成型。